Board of Supervisors

| W. Canova Peterson, Chairman Mechanicsville District | Hanover Courthouse | Department of Public Works |
| --- | --- | --- |
| Scott A. Wyatt, Vice-Chairman Cold Harbor District |  | J. Michael Flagg, P.E., Director W. R. Hardman, III, P.E., Deputy Director |
| Sean M. Davis Henry District |  | P.O. Box 470 7516 County Complex Road |
| Wayne T. Hazzard south anna District |  | Hanover, Virginia 23069 Phone: 804-365-6181 |
| Angela Kelly-Wiecek chickahominy District |  | Fax: 804-365-6233 www.hanovercounty.gov |
|  | HANOVER COUNTY Established in 1720 |  |
| Faye O. Prichard ashland District |  | Cecil R. Harris, Jr. County Administrator |
| Aubrey M. Stanley beaverdam District |  | Frank W. Harksen, Jr. Deputy County Administrator |

Date July 25, 2019

Goodfellow, Jalbert, Beard & Associates, Inc.

ATTN:  Bonnie Beavers

P.O. Box 539

Mechanicsville, VA 23111

RE:	Watts RV & Boat Storage

SPR # 2019-00031

E&S # 5499

BP # 19-09900031

Dear Ms. Beavers,

The Department of Public Works has reviewed the above captioned site plan submission and would like to offer the following comments; Please note, these comments have been submitted based on the requirements of the following Virginia State Laws and Hanover County Codes: Chapter 10, Article V, Stormwater Management, Chapter 10, Article I, Erosion and Sediment Control, Code of Hanover; Chapter 10, Article II, Chesapeake Bay Preservation, Code of Hanover; Chapter 12, Floodplain and Drainage Control, Code Of Hanover; and the Hanover County Drainage Design Handbook (February 12, 2014):

(ALL PREVIOUSLY MADE COMMENTS IN ITALICS)

General

- The E&S inspection fee is based on the amount of land disturbance certified on the cover sheet of the plan (3.52 acres [note limit of 10 acres max]).  Please note that the Erosion and Sediment Control (E&S) fee for this project must be paid prior to issuance of the land disturbance permit.  The fee has been calculated to be $1689.12, which is an increase of $443.70 from the original fee amount. This fee is based on the current fee rate of $612.00 minimum base fee, plus $306.00 per acre ($3,672.00 maximum fee). You must provide the cashier with the HTE project tracking number to facilitate the payment process. Please submit payment to the cashier located in the Commissioner of Revenue Office.  Do not submit payment to the Department of Public Works. PLEASE NOTE: Any increase / decrease in the proposed acreage of land disturbance will change the aforementioned fee.  Also, since the E&S inspection fees are due at time of plan approval, any plan approved after the date on which a fee base increase is enacted will be subject to that increase.

- An amended E&S bond will be required prior to issuance of the Amended Land Disturbance Permit.  The bond amount is determined based on the amount of E&S controls required for the project.  The amended bond has been calculated to be $18,904.00 for combined E&S measures.  This bond amount is subject to change if E&S quantities change with project design.  The bond may be in the form of cash, irrevocable letter of credit, or surety and must be on the County format (please check with your lender to ensure they have the correct forms).  The bond form (cash, ILC, or surety) must be completed, notarized and submitted to this department with the bond amount prior to any land disturbing activities on site.  E&S bonds will be held by this department until the site work is complete and there is a minimum 85% established healthy vegetation over all non-hardened or denuded surfaces.  Please submit revised bond for amount listed above.

- It appears land disturbance is being increased from 2.07 acres to 3.54 acres.  Please provide an amended copy of your “VSMP General Permit Registration Statement- Construction Activity Stormwater Discharges (DCR01).”   Hanover is the authority for issuance of these permits.  A separate payment will have to be made to Virginia DEQ at the time of permit certification by the County.  We will provide you notification when the permit has been certified.

- Please submit two copies of an amended Stormwater Pollution Prevention Plan (SWPPP) that meets the requirements of Part II A of the VSMP Construction General Permit (9 VAC 25-880). A review of this document will be performed in order to ensure that the SWPPP meets regulatory requirements.  We will need these two copies of the SWPPP before a land disturbance permit can be issued.  A SWPPP template is available from the review engineer upon request.

- It appears 0.10 acres of wetlands will be disturbed.  Please provide a USCOE verification of the wetland delineation and evidence of the USCOE permit prior to site plan approval.

- It appears that Water Quality requirements are met by purchasing credits.  Please be aware that these credits will need to be acquired in a manner that is consistent with Section 62.1-44.15:35 of the Code of Virginia.  The credits will need to come from a DEQ non-point source approved vendor and shall be generated in the same or adjacent eight-digit hydrologic unit code of the same tributary.  At a minimum, a letter of availability from the credit vendor will need to be provided on the plan prior to plan approval.  This letter will need to document the number of phosphorus nutrient credits to be acquired and the associated ratio of nitrogen nutrient credits.  A bill of sale will need to be provided before a land disturbance permit can be issued.

- Please add the plan project numbers SPR # 2019-00031, BP # 19-09900031, and E&S # 5499 to the cover sheet.

- Please provide deed book and page numbers for Stormwater Management Basins #1 and #2 on the plan sheets C-4 and C-5.

- Please move the following items from sheet C-6 to the cover sheet:

- Land disturbance and impervious area statement. (Sign)

- Mapping resources and site analysis statement. (Sign)

- Please provide the Stormwater Best Management Practices Spreadsheet showing SWM # 2 calculations on the plans (sheet C-7).

- Please provide clarification of grading and drainage behind phase III structure.

E&S

- Please label each pre and post development drainage area on all maps with acreage and the associated C factor.  Please provide pre and post development drainage area maps on a 1”=50’ scale (maximum).

- Provide a phased erosion and sediment control plan.  Phase I should show the initial area of disturbance in the Watt’s Grading Plan.  Phase II can show the ultimate limits of disturbance, proposed grading, proposed site improvements, etc.  Please show all E&S controls for each phase in relation to existing contours and drainage patterns.

- Provide a detailed Erosion and Sediment Control measure quantity list for each phase.

- Phase 1 quantity list: existing measures of the Watt’s Grading Plan

- Phase 2 quantity list: additional measures of the Watt’s RV and Boat Storage Plan

- Please provide a more detailed E&S Narrative, by providing the following information on the plan:

- Please summarize the Watt’s Grading Plan (stockpile plan) as part of the plan as E&S control plan phase 1 of a 2 Phase E&S control plan.

- Please state that E&S controls may be removed only upon the approval of the Hanover County Public Works E&S inspector. They may be contacted at (804) 365-6181.

- Please change all references to county engineer, environmental inspector, county engineer, local county officials, etc. that appear throughout the E&S notes and narratives to “Hanover County Public Works E&S inspector”.

If you should have any questions concerning the detailed comments made during the review of your plans, please give me a call at 365-6181.  When resubmitting plans, please return a copy of these comments with a note stating how/where each comment was addressed.

Sincerely,

Nicole Onellion, E.I.T.

Civil Engineer I

Department of Public Works

Cc:  	Morse Code, LLC

ATTN: Eddie Watts

7380 Chestnut Church Road

Mechanicsville, VA 23116

Megan Dalzell, Planning Department