Board of Supervisors

| W. Canova Peterson, Chairman Mechanicsville District | Hanover Courthouse | Department of Public Works |
| --- | --- | --- |
| Scott A. Wyatt, Vice-Chairman Cold Harbor District |  | J. Michael Flagg, P.E., Director W. R. Hardman, III, P.E., Deputy Director |
| Sean M. Davis Henry District |  | P.O. Box 470 7516 County Complex Road |
| Wayne T. Hazzard south anna District |  | Hanover, Virginia 23069 Phone: 804-365-6181 |
| Angela Kelly-Wiecek chickahominy District |  | Fax: 804-365-6233 www.hanovercounty.gov |
|  | HANOVER COUNTY Established in 1720 |  |
| Faye O. Prichard ashland District |  | Cecil R. Harris, Jr. County Administrator |
| Aubrey M. Stanley beaverdam District |  | Frank W. Harksen, Jr. Deputy County Administrator |

October 2, 2019

Jordan Consulting Engineers, P.C.

ATTN:  Piotr “Peter” Matysiak

2540 Professional Road

Richmond, VA 23235

RE:	Northlake 95 Business Center

SPR # 2019-00033

E&S # 5506

PWLDC # 2019-00014

Dear Mr. Matysiak,

The Department of Public Works has reviewed the above captioned site plan submission and would like to offer the following comments; Please note, these comments have been submitted based on the requirements of the following Virginia State Laws and Hanover County Codes: Chapter 10, Article V, Stormwater Management, Chapter 10, Article I, Erosion and Sediment Control, Code of Hanover; Chapter 10, Article II, Chesapeake Bay Preservation, Code of Hanover; Chapter 12, Floodplain and Drainage Control, Code Of Hanover; and the Hanover County Drainage Design Handbook (February 12, 2014):

(ALL PREVIOUSLY MADE COMMENTS IN ITALICS)

General

- The Erosion and Sediment Control (E&S) Inspection Fee for this project must be paid prior to issuance of the land disturbance permit.  This fee has been determined to be $3,672.00.  This fee has been based on the certified disturbed acreage amount of 26.13 acres on the cover sheet of the plans and the current fee schedule of $612.00 base fee + $306.00/disturbed acre (first 10 acres/max $3,672.00).  Please submit payment to the cashier located in the Commissioner of Revenue Office.  Do not submit payment to the Department of Public Works. PLEASE NOTE: Any increase / decrease in the proposed acreage of land disturbance will change the aforementioned fee.  Also, since the E&S inspection fees are due at time of plan approval, any plan approved after the date on which a fee base increase is enacted will be subject to that increase.

- An E&S bond will be required prior to issuance of the Land Disturbance Permit.  The bond amount is determined based on the amount of E&S controls required for the project.  This fee has been determined to be $145,508.00.  This bond amount is subject to change if E&S quantities change with project design.  The bond may be in the form of cash, irrevocable letter of credit, or surety and must be on the County format (please check with your lender to ensure they have the correct forms).  The bond form (cash, ILC, or surety) must be completed, notarized and submitted to this department with the bond amount prior to any land disturbing activities on site.  Note: Surety requires the first $20,000.00 to be in the form of cash or letter of credit.  E&S bonds will be held by this department until the site work is complete and there is a minimum 85% established healthy vegetation over all non-hardened or denuded surfaces.

- Provide a copy of your “VSMP General Permit Registration Statement- Construction Activity Stormwater Discharges (DCR01)”.  Hanover is the authority for issuance of these permits.  A separate payment will have to be made to Virginia DEQ at the time of permit certification by the County.  We will provide you notification when the permit has been certified.

- Please submit two copies of a Stormwater Pollution Prevention Plan (SWPPP) that meets the requirements of Part II A of the VSMP Construction General Permit (9 VAC 25-880).  A review of this document will be performed in order to ensure that the SWPPP meets regulatory requirements.  We will need these two copies of the SWPPP before a land disturbance permit can be issued.  A SWPPP template is available from the review engineer upon request.

- Please provide a USCOE verification of the wetland delineation and evidence of the USCOE permit prior to site plan approval.  Final application for wetland impacts and approved permit are required.

- A Land Use Permit will be required from VDOT for any work that takes place in their right-of-way.

BMPs and Drainage

- A basin maintenance agreement must be recorded with deed book and page number depicted on the plan prior to site plan approval.  In addition to the facility maintenance, a professional engineer must inspect the on-site facility / dam (including outlet works) during the last 60 days of the first year of operation, and at least once every five years thereafter.  The engineer’s inspection report must be subsequently submitted to Hanover County DPW for their review.

- Please correct the forebay volume calculations to reflect 40% minimum per Table 14.2 of the Virginia Stormwater BMP Clearinghouse.

- Provide flow path details on basin to show design requirements are met per Table 14.2 of the Virginia Stormwater BMP Clearinghouse.

- Provide clay linear specifications to plan sheets and reference specifications in the BMP Clay Linear Note on sheet C8.2.

- Soil borings should be taken to determine physical characteristics of the soil, determine depth of the groundwater table, and evaluate potential infiltration losses/need for a liner per Virginia Stormwater BMP Clearinghouse Design Specification No. 14 Section 6: Design Criteria.

- Provide valve and discharge pipe details and specifications.  It is not clear where discharge pipe is and how dewatering structure operates.

- Provide pond-landscaping details the area outside the aquatic bench and on the aquatic bench.  Ensure landscaping provided is to discourage geese.

- Please provide aeration (bubbler) to the BMP design per Table 14.2 of the Virginia Stormwater BMP Clearinghouse.  In addition, provide details and specifications in plan sheets.

- Please revise drainage easements near North Lakeridge Parkway entrance as shown on the easement plat.

If you should have any questions concerning the detailed comments made during the review of your plans, please give me a call at 365-6181.  When resubmitting plans, please return a copy of these comments with a note stating how/where each comment was addressed.

Sincerely,

Nicole Onellion, E.I.T.

Civil Engineer I

Department of Public Works

Cc:  	Northlake Land Investments, LLC

ATN: Gibson Wright

1503 Santa Rosa Road, Suite 103

Richmond, VA 23229

John Jordan, Jordan Consulting Engineers, P.C.

Megan Dalzell, Planning Department